## Slide 1
Magali Blanco, PhD
Env. and Occ. Health Sciences, School of Public Health
magali@uw.edu
Amanda Gassett, Timothy Gould, Annie Doubleday, David L. Slager, Elena Austin, Edmund Seto, Timothy Larson, Julian D. Marshall, Lianne Sheppard
Funding: ACT – Air Pollution Study (National Institute of Environmental
Health Sciences; National Institute on Aging, R01ES026187)
Characterizing Ultrafine Particulate Matter and Black Carbon Exposure Levels for a Seattle-Based Cohort From a Mobile Monitoring Campaign
Notes: -Work was conducted as part of my dissertation
-funded: NIEHS; NIA
-I’ll cover some background before describing the work we conducted

## Slide 2: Adult Changes in Thought (ACT) Study
Seattle-based prospective cohort study investigating aging and the brain
  Started in 1994
Participants
  Elderly individuals (65+ yr)
  Dementia-free at baseline
Participants are followed until they are diagnosed with dementia
Top: Huges 2018. Bottom: Bowles 2019. ACT study visit – grip strength test.
Notes: An ideal cohort to study long-term air pollution exposure & dementia incidence

## Slide 3: Mobile Monitoring
Collect repeated short-term samples used to estimate long-term averages
  Time- and cost- efficient
    Site sampling duration can be very short
    Increased spatial coverage
    One platform
  Convenience sampling
    Short time periods (e.g., Mon-Fri)
    Non-residential areas (e.g., highways, industry)
    Mobile, on-road samples (vs. stationary samples near residences)
Top to bottom: 1) Instrumentation in the mobile monitoring vehicle. 2) Sampling inlet on vehicle rooftop. Photograph by Sarah Fish, fischs@uw.edu. 3) Mobile monitoring vehicle.
Notes: * We were interested in using mobile monitoring to assess air pollution exposure
# References
• Mobile monitoring campaigns to characterize average air pollution levels (Apte et al. 2017; Hatzopoulou et al. 2017; Kerckhoffs et al. 2016; Messier et al. 2018; Xie et al. 2017)

## Slide 4: Study Overview
Conducted a mobile monitoring campaign to measure annual-average traffic-related air pollution levels for the ACT cohort
Built UFP and BC prediction models
Characterized exposure for the ACT cohort and the greater Seattle area
Photograph by Sarah Fish, fischs@uw.edu.

## Slide 5: Our Mobile Monitoring Campaign
Purpose: Address past monitoring limitations
309 stop locations representative of ACT cohort (large, geographically diverse area)
9 fixed driving routes
2-min samples per stop
Measured UFPs, BC, PM2.5, CO, CO2, NO2
A driving schedule ensured temporally balanced sampling
Top: Jittered ACT locations and monitoring stops. Bottom: Mobile monitoring routes and stops

## Slide 6: Final Samples
Collected ~27 samples per site
  5 AM – 12 AM
  March 2019 – March 2020
  >270 drive days
Left: Instruments inside the vehicle. Right: Monitoring laptop. Photograph by Sarah Fish, fischs@uw.edu.
Notes: This was a fairly extensive campaign

## Slide 7: Sampling Approaches Across Other UFP Studies
Compared to other similar studies, we had:
  More sites
  more repeat visits
  Shorter visits
Similar for BC
Notes: To put this into perspective, we can compare some of the features of our study design to other studies. On the x-axis you have studies stratified by the type of sampling type that was conducted…3 types…Our study is in teal. We can see that overall, we generally sampled more study sites, visited each site more times even though we were there for shorter periods of time

## Slide 8: Instrumentation
UFPs: P-TRAK 8525 (TSI)
  Time resolution: 1 sec
  Particle size range: 20-1,000 nm diameter
BC: MicroAeth, MA200 (AethLabs)
  Time resolution: 10 sec
  Wavelength: 880 nm (IR)
Top: P-TRAKs in the monitoring vehicle.
Bottom: MicroAethalometers (AethLabs, 2018).

## Slide 9: Annual Averages
Calculated site annual averages using linear regression to address unbalances in data
Annual average UFP estimates from mobile monitoring observations.
Notes: The first step of this analysis involves data reduction.
Median site visit concentrations
Trimmed extreme observations at each site
The first step of this analysis involves data reduction. We have 1-sec measurements that we want to convert to an annual average.
• extreme observations may be overly influential b/c of our small sample size. They may be
a) rare (e.g., temporary construction)
b) a result of instrument error
𝑻𝑹𝑨𝑷= 𝜷_𝟎+𝜷_𝟏 𝑰_𝑺𝒊𝒕𝒆+𝜷_𝟐 𝑰_𝑺𝒆𝒂𝒔𝒐𝒏+ 𝜷_𝟑 𝑰_𝑻𝑶𝑾𝟐 +𝜷_𝟒 𝑰_𝑻𝑶𝑫𝟓+ 𝜀

## Slide 10: Prediction Models
Built universal kriging (UK) models using partial least squares (PLS) and geostatistical smoothing (kriging):
where are the PLS component scores; and are estimated model coefficients; is the residual term with mean zero and a geostatistical structure modeled as an exponential function with range 𝜙𝑖, partial sill 𝜎𝑖, and nugget 𝜏𝑖
Notes: PLS summarized hundreds of geographic covariates into a smaller number of new features
Kriging allows for spatial correlation in the data…Models part of the structure that resides in error term not otherwise captured by regression

## Slide 11: Predicted UFP and BC Exposure Surfaces
Higher predicted concentrations between downtown and the airport, on highways

## Slide 12: Differences in UFP and BC Surfaces
Can BC be used as a surrogate for UFP?
UFP levels at some locations are mischaracterized more when using BC models (large residuals)

## Slide 13: Differences in UFP and BC Surfaces
Plotting the difference between UFP observations and predictions based on BC models (residuals)
UFP levels were:
(+): Sea-Tac Airport
(-): Rail yards, large ports
UFP residuals for UFP-BC linear regressions using estimates (from mobile monitoring observations) and model predictions (at grid locations). Black circles are locations with high residuals (< 5th quantile or > 95th quantile); black lines are railroads. Residual predictors were selected using Lasso regression.

## Slide 14: Conclusions
First to characterize the long-term UFP and BC exposure surface with high spatial resolution for the greater Seattle area
  Innovative mobile monitoring campaign specifically designed for epidemiologic application
Differentiated UFP and BC surfaces
Next steps: use of these models in epidemiologic studies
Top: UFP predictions from the Seattle area. Bottom: Our mobile monitoring vehicle. Photograph by Sarah Fish, fischs@uw.edu.
Notes: * Our study may be the largest in terms of:
  Spatial extent covered
  Sampling density
  Sampling frequency & duration

## Slide 15: Acknowledgements
PhD Committee
  Lianne Sheppard
  Edmund Seto
  Tim Larson
  Sara Adar
  Julian Marshall
Mobile monitoring team
  Amanda Gassett
  Jim Sullivan
  Dave Hardie
  Tim Gould
Additional Support
  Brian High
  Elena Austin
  ACT-AP team
  Gail Li
  Paola Filigrana
Funding
  ACT – Air Pollution Study (NIEHS, NIA, R01ES026187)
  BEBTEH: Biostatistics, Epidemiologic & Bioinformatic Training in Environmental Health (NIEHS, T32ES015459)
  ARCS Foundation Fellowship
Contact:
Magali Blanco, PhD
Environmental and Occupational Health Sciences, School of Public Health
magali@uw.edu

## Slide 16: Image Credits
AethLabs. 2018. microAeth MA200 Tech Specs. https://aethlabs.com/sites/all/content/microaeth/ma200/microAeth%20MA200%20Specifications %20Sheet%20Rev%2001%20Updated%20Aug%202018.pdf
Bowles. 2019. The ACT study: Looking toward the future. Kaiser Permanente. https://www.kpwashingtonresearch.org/news-and-events/blog/2019/august-2019/act-study-looking-toward-future
Hughes. 2018. ACT study: Long-running study of aging examines changes in Kaiser Permanente patients over time. Kaiser Permanente. https://www.kpwashingtonresearch.org/our-research/research-areas/aging-geriatrics/act-study-long-running-study-aging-examines-changes-kaiser-permanente-patients-over-time
King County Metro. 2020. Where will people live in 2040? http://www.kcmetrovision.org/king-county-in-2040/where-will-people-live/

## Slide 17: Appendix

## Slide 18: Monitoring Stops & ACT Locations
Stop locations and ACT residences had similar geocovariate distributions (spatial compatibility)
Left: density plots of geocovariate distributions for monitoring stops and ACT locations. Right: Map of jittered ACT locations and monitoring stops.

## Slide 19: Instrument Specifications
Parameter | Instrument | Manufacturer | Measurement Range | Limit of Quantification | Time Resolution
Particles |  |  |  |  | 
UFP |  |  |  |  | 
10-420 nm (and 13-bin PSD) | NanoScan 3910 | TSI | 102-106 pt/cm3 | 10 pt/ cm3 | 60 sec
10-700 nm | DiSCmini | Testo | 103-106 pt/cm3 | 500-2,000 pt/cm3 b | 1 sec
20-1,000 nm | PTRAK 8525 | TSI | 0 - 5 x 105 pt/cm3 | 1 pt/cm3 | 1 sec
50-1,000 nm | PTRAK 8525, with diffusion screen | TSI | 0 - 5 x 105 pt/cm3 | 1 pt/cm3 | 1 sec
BC & UV PM (5 wavelength abs analysis) | microAeth MA200 | AethLabs | 0-1 mg BC/m3 | 30 ng BC/m3 c | 10 sec
Light scattering extinction coef (PM2.5) | M903 | Radiance Research | 0 - >1 km-1 | 10-6 m-1 | 10 sec
Gases |  |  |  |  | 
NO2 | CAPS NO2 | Aerodyne Research, Inc. | 0-2,000 ppb | 2 ppbv | 1 sec
CO2 | SenseAir CO2 K-30-FS sensor | CO2Meter.com | 0-5,000 ppm (vol) | 100 ppmv | 1 sec
CO | CO Monitor T15N | Langan, Inc. | 0-200 ppm | 0.1 ppm | 1 sec
Other |  |  |  |  | 
Temperature | Onset UX100-011 | HOBO | -4-158°F |  | 1 sec
Relative humidity | Onset UX100-011 | HOBO | 0-95% |  | 1 sec
Positioning & real-time tracking | DG-500 | US GlobalSat | 0-515 m/sec speed | 2.5 m | 1 sec

## Slide 20: Strong UFP and BC Predictors
Length of major roads
Population density
Land development, imperviousness
NDVI, green space
Distance to large port, rail yard
In line with literature
PLS component loadings for UFP model

## Slide 21: Exposure Predictions for the ACT Cohort
A large degree of exposure variation
Low levels
  Seattle’s air
  Similar to rural/suburban locations
  Wider geographic area & sampling times
Pollutant | Median | Range
UFP (pt/cm3) | 6,782 | 2,491-15,682
BC (ng/m3) | 525 | 232-1,130
Estimated mean/median UFP and BC concentrations from other studies. Gray dots and vertical lines are the median and range.
Notes: Though it is difficult to compare UFP lvls across studies b/c studies use different size ranges, based on instrumentation
  Though our analyses did not show any clear reason for large coc discrepancies between studies when we compared instruments used and the concentrations reported by those studies
  EPA has noted this as a limitation in the field
REFS
*BC levels:
Sources: Oakland, CA: Apte et al. 2017; The Netherlands: Kerckhoffs et al. 2016 & 2017, Montagne et al. 2015; Toronto, CA: Minet et al. 2018; New Delhi, India: Saraswat et al. 2013

## Slide 22: Limitations
Mobile monitoring stop averages may be noisy (27 two-min samples/site)
  ≤20% error
Regression approach for estimating annual averages assumes that sites have similar temporal trends
Limited built environment covariates that may impact dispersion (e.g., street width)
  But does include correlated covariates (e.g., population)

## Slide 23: Model Performances
Higher R2 model performance than similar studies
Similar for BC
Model performance from other UFP studies. Gray dot and vertical line are the median and range; this study is in blue; other studies are in red.
Notes: high model performance is an important strength for TRAPs, which have strong decay patterns – models captured exposure surfaces well
We reported MSE-based CV R2. Others have likely reported an in-sample regression-based R2 (most did not state), which should perform better.