## Slide 1: Ambient Ultrafine Particles Near Sea-Tac Airport
Timothy Larson, Edmund Seto, Elena Austin, Timothy Gould, Michael Yost
University of Washington, Seattle
Presentation to the Federal Way Transportation & Planning Commission
April 1, 2019

## Slide 3
Health Effects more uncertain compared to PM2.5 ,but a growing body of evidence
Diesel Engines emit ultrafine particles resulting in elevated levels near major roadways (within 200 meters downwind)
Ultrafine Particles unregulated but potentially important
Ultrafine Particles (UFPs)
Jet aircraft emissions emit “ultra-ultra fine” particles (< 30 nanometers)

## Slide 4
Occupational exposures to UFP are known to be high in some settings.
Moller et al (2014) PLoS ONE 9(9): e106671, doi:10.137/journal.pone.006671
A map of personal exposure concentrations for workers at the Copenhagen airport in Autumn of 2012 is shown at right.

## Slide 5
Hudda et al, ES&T 2014; Hudda and Fruin, ES&T 2016
103/cc
Particle size between ~10 and 30 nm diameter are still present at high concentrations at ground level
at 16 km downwind
“Ultra-Ultrafine” Particles

## Slide 6: A selection of cities with published studies of airport UFP impacts
Distance from airport to monitoring site |  | 
< 1km | 1 to 10 km | > 10 km
Tianjin, China | London, England | Los Angeles, CA
Rome, Italy | Los Angeles, CA | Amsterdam, NL
Venice, Italy | Norwich, England | Atlanta, GA
Taipei, Taiwan | Boston, MA | New York, NY*
Oakland, CA | Warwick, RI | 
Santa Monica, CA |  | 
*La Guardia

## Slide 7
Randomized crossover study of 22 non-smoking adults with mild to moderate asthma
2-hr scripted, mild walking activity both inside and outside of the high LAX UFP impact zone (avg. difference ~30,000 /cc)
Mean particle size at LAX impact zone was 29 nm
“We found significant increases in markers of systemic inflammation associated with ‘Airport UFPs’ and ‘Traffic’ exposure

## Slide 8: UFP Monitoring Instruments
Increasing Reliability & Cost
Scanning Mobility Particle Sizer
Water-based CPC
Electrostatic Sizing
2nm – 1000 nm
>100 size bins
15 second readings
Nanoscan
Alcohol-based CPC
Electrostatic Sizing
10nm – 300 nm
16 size bins
1-minute readings
Condensation Particle Counter
Alcohol-based CPC
> 7nm total count
No Sizing
1 second readings
DiSC mini
Electrostatic
10 nm – 300 nm
Average size & total count
1 second readings

## Slide 9: MOV-UP Study Mobile ObserVations of Ultrafine Particles (MOV-UP) Study

## Slide 10: Instruments used in mobile and fixed location sampling
Parameter | Instrument
Particle number concentration (10 nm – 1 µm) | Condensation Particle Counter 3007
Particle size distribution, 13 bins | NanoScan 3910
Black Carbon PM | Micro-Aethalometer AE51
CO2 | LI-820 Gas Analyzer
Position & Time tracking | GPS Receiver DG-500

## Slide 11
Study Region and Fixed
Monitoring Site Locations

## Slide 12: “Roadway” Feature
Wind from the SOUTH
Wind from the NORTH
Winter – Spring Data
Notes: Add airplane and wind

## Slide 13: “Ultra-UFP” Feature
Wind from the SOUTH
Wind from the NORTH
Winter – Spring Data
Notes: Difference of ratios? Add roadway

## Slide 14: “Ultra-UF” Feature Winds from the SOUTH
Predicted*
Observed*
Median Income
**Average over all hours on all sampling days
*Average of all hours during daytime sampling periods

## Slide 15: “Ultra-UF” Feature Winds from the NORTH
Observed *
Predicted **
**Average over all hours on all sampling days
*Average of all hours during daytime sampling periods
Median Income

## Slide 16: Monitoring Locations: Schools
Scientifically Relevant (in or out of plume?)
Relevant to Communities
Long-term Availability
Adequate infrastructure
  Power
  Space
  Security
  Ease of access for operating instruments

## Slide 17
Monitoring Locations: Schools

## Slide 18
Monitoring Locations: Schools

## Slide 19: Summary
Ultrafine Particles (UFPs) are observed near busy roadways and also up to ~10-15 km downwind of SeaTac Airport
Additional monitoring is needed to support health impact studies near the airport
Predictions from a standard atmospheric dispersion model can help to design a UPF monitoring network near the airport
Public schools are good candidates for UFP monitoring sites

## Slide 20
Questions?

## Slide 22: Supplemental Slides (if questions arise)

## Slide 23: New Beacon Hill Study
Select at least one site in Beacon Hill for simultaneous ultrafine particle (UFP) and noise sampling.
Set up an “anchor site” for comparison that we know is impacted by aircraft UFP and noise.
Run both sites simultaneously so that we can make comparisons for different flight characteristics (traffic, time of day, etc.)

## Slide 24: Emission Factors # Particles/[CO2]mass
Quantiles of PCA (Ultra-UF)
Quantiles of PCA (Roadway)
Winter – Spring Data
Notes: Add emission by quintile of propSmall

## Slide 25
Recent Studies Suggesting Acute Health Effects in Susceptible Populations
Exposures Documented with Personal Monitors
Controlled Exposures to Concentrated Ambient Particles

## Slide 26
Southerly Winds
Wind (majority)
Aircraft

## Slide 27
Northerly Winds
Wind
Aircraft

## Slide 28
“Fine” Particles

## Slide 29
5 mg/m3
10 mg/m3
15 mg/m3
25 mg/m3
20 mg/m3
35 mg/m3